Sauce Making Machine

This sauce making machine is an electric machine using for making sauce, like tomato sauce, strawberry sauce, mango sauce and so on . It is easy to operate and save energy and time.

Part List

1. Holding bowl
2. Pusher tool
3. Grinder
4. Grinder cover
5. Exit tray
6. Grinder connector
7. Spring
8. Spare gear9. Splash guard

Assembly Instructions

1. Attach spring (7) to the plastic end of the grinder connector (6).

2. Insert the grinder connector (6) metal end first into the grinder hole on the machine.

3. Insert the grinder (3) into the grinder hole and then install the grinder cover (4) over it. Turn the cover until it locks into place.

4. Install the holding bowl (1) on top of the machine.

4. Install the splash guard (9) onto the exit tray (5) and then hook them onto the grinder cover (4).

Full installation video link:

https://www.youtube.com/watch?v=BGCzXSL1oIA

Notes

Before using a dish washer, it should be cleaned of any food particles first.

Technical Specifications

| Model | GRT-ETC-1 |
| --- | --- |
| Voltage | 110V/220V |
| Power | 370W |
| Dimension | 490*230*345mm |
| Weight | 8.5kg |
| Productivity | 15-30kgs/h |
| Sauce Output | 85% |
| Motor | copper motor |

SAUCE MAKING MACHINE

.......................................................................

USER’S MANUAL